ENGINE FAILURE DURING TAKEOFF

- Throttle	IDLE

- Brakes	APPLY

- Wing Flaps	RETRACT

- Mixture	IDLE CUT-OFF

- Ignition Switch	OFF

- Master Switch	OFF

##### ENGINE FAILURE AFTER TAKEOFF

- Airspeed	 80 MPH

- Mixture	IDLE CUT-OFF

- Fuel Selector Valve	OFF

- Ignition Switch	OFF

- Wing Flaps	AS REQUIRED

- Master Switch	OFF

ENGINE FAILURE DURING FLIGHT

- Airspeed	85 MPH

- Carburetor Heat	ON

- Fuel Selector Valve	BOTH

- Mixture	RICH

- Ignition Switch	BOTH or START

- Primer	IN & LOCKED

EMERGENCY LANDING

- Airspeed	 80 MPH

- Mixture	IDLE CUT-OFF

- Fuel Selector Valve	OFF

- Ignition Switch	OFF

- Wing Flaps	AS REQUIRED

- Master Switch	OFF

- Doors	UNLATCH PRIOR TO TOUCHDOWN

- Touchdown	SLIGHTLY TAIL LOW

- Brakes	APPLY HEAVILY

###### PRECAUTIONARY LANDING

- Wing Flaps	15(

- Airspeed	75 MPH

- Select field	SUITABLE

- Avionics Power Switch	OFF

- Electrical Switches	OFF

- Wing Flaps (on final approach)	30(

- Airspeed	75 MPH

- Master Switch	OFF

- Doors	UNLATCH PRIOR TO TOUCHDOWN

- Touchdown	SLIGHTLY TAIL LOW

- Ignition Switch	OFF

- Brakes	APPLY HEAVILY

# CABIN

- Pilot’s Operating Handbook	AVAILABLE

- Aircraft Documents 	 AVAILABLE

- Control Wheel Lock	REMOVE

- Ignition Switch	OFF

- Avionics Power Switch	OFF

- Master Switch	ON

- Fuel Quanity Indicators	CHECK QUANTITY

- Flaps	DOWN

- Master Switch	OFF

# EMPENNAGE

- Rudder Gust Lock	REMOVE

- Tail Tie-Down	DISCONNECT

- Control Surfaces	CHECK FREE

# RIGHT WING

- Aileron	CHECK FREE

- Wing Tie-Down	DISCONNECT

- Main Wheel Tire	CHECK

- Fuel Tank Sump	SAMPLE

- Fuel Quantity	CHECK

- Fuel Filler Cap	SECURE

NOSE

- Engine Oil Level	CHECK

- Fuel Strainer	DRAIN

- Propeller and Spinner	CHECK

- Landing Light	CHECK

- Carburetor Air Filter	CHECK

- Nose Wheel Strut and Tire	CHECK

- Static Source Opening	CHECK

### LEFT WING

- Main Wheel Tire	CHECK

- Fuel Tank Sump	SAMPLE

- Fuel Quantity	CHECK

- Fuel Filler Cap	SECURE

- Pitot Tube Cover	REMOVE

- Fuel Tank Vent Opening	CHECK

- Stall Warning Opening	CHECK

- Wing Tie-Down	DISCONNECT

- Aileron	CHECK FREE

BEFORE STARTING ENGINE

### Preflight Inspection	COMPLETE

### Seats, Belts, Shoulder Harnesses

### ADJUST & LOCK

### Fuel Selector Valve	BOTH

### Avionics Power Switch	OFF

### Electrical Equipment	OFF

### Brakes	TEST & SET

### Circuit Breakers	CHECK IN

### Cowl Flaps 	 OPEN

STARTING ENGINE

- Hobbs Time 	 RECORD

- Mixture	RICH

- Propeller 	 HIGH RPM

- Carburetor Heat	COLD

- Master Switch	ON

- Prime	AS REQUIRED

- Throttle	OPEN ½ INCH

- Propeller Area	CLEAR

- Ignition Switch	START

- Throttle	1000 RPM

- Oil Pressure	CHECK

- Flashing Beacon, Nav. Lights	ON

- Avionics Power Switch	ON

- Radios	ON

- Transponder	STANDBY

#### BEFORE TAXI

- Wing Flaps	UP

- Parking Brake	RELEASE

- Brakes	TEST

- Area	CLEAR

BEFORE TAKEOFF

- Parking Brake	SET

- Cabin Doors and Windows

CLOSED & LOCKED

- Flight Controls	FREE & CORRECT

- Flight Instruments	SET

- Fuel Selector Valve	BOTH

- Mixture	(Below 3000’) RICH

- Stabalator Trim	TAKEOFF

- Rudder Trim (if installed)	TAKEOFF

- Throttle	1800 RPM

- Magnetos	CHECK

- Propeller 	 CYCLE

- Auxiliary Fuel Pump	CHECK

- Engine Instruments	CHECK

- Ammeter	CHECK

- Suction Guage	CHECK

- Throttle	1000 RPM

- Radios	SET

- Transponder	ON-ALT

## NORMAL TAKEOFF

- Wing Flaps	0( - 10(

- Carburetor Heat	COLD

- Throttle	FULL OPEN

- Propeller 	 2700 RPM

- Elevator Control	LIFT NOSE AT 60 MPH

- Climb Speed	BEST RATE

#### SHORT FIELD TAKEOFF

- Wing Flaps	10(

- Carburetor Heat	COLD

- Brakes	APPLY

- Throttle	FULL OPEN

- Propeller 	 2700 RPM

- Mixture	LEAN above 3000’, RICH below 3000’

- Brakes	RELEASE

- Elevator Control	SLIGHTLY TAIL LOW

- Climb Speed (Until Obstacles Cleared) 	69 MPH

#### ENROUTE CLIMB

- Airspeed	90-100 MPH

- Power	24” –Full Power, 2500-2700 RPM

- Mixture	LEAN above 3000’, RICH below 3000’

- Cowl Flaps 	 OPEN AS REQUIRED

CRUISE

- Power	75% or LESS

- Stabilator Trim	ADJUST

- Rudder Trim (if installed)	ADJUST

- Mixture	LEAN

- Cowl Flaps 	 CLOSED

DESCENT

- Fuel Selector Valve	BOTH

- Mixture	ADJUST

- Power	AS DESIRED

- Carburetor Heat	FULL AS REQUIRED

#### BEFORE LANDING

- Seats, Belts, Shoulder Harnesses	SECURE

- Fuel Selector Valve	BOTH

- Mixture	RICH

- Propeller 	 HIGH RPM

- Carburetor Heat	ON

- Airspeed 	 80-90 MPH

- Flaps 	AS DESIRED

## BALKED LANDING

- Power	FULL THROTTLE, 2700 RPM

- Carburetor Heat	COLD

- Wing Flaps	(immediately) 20(

- Climb Speed	BEST ANGLE

- Wing Flaps (after safe alt. and 75 MPH)

RETRACT

#### AFTER LANDING

- Wing Flaps	UP

- Carburetor Heat	COLD

- Cowl Flaps 	 OPEN

- Transponder	STANDBY

#### SHUTDOWN

- Parking Brake	SET

- Avionics Power Switch	OFF

- Electrical Equipment	OFF

- Mixture	IDLE CUT-OFF

- Ignition Switch	OFF

- Master Switch	OFF

- Control Lock	INSTALL

- Fuel Selector Valve 	 RIGHT

Aeroclub of Chania

Κρατικός Αερολιμένας Χανίων

Τηλέφωνο και ΦΑΞ

2821027272

Γραφείο Πτήσεων

ΤΗΛ. 6972702900

### Email:	aer@aer.gr

### Internet:	www.aer.gr

# Text boxes

### Speeds for Normal Operation

Vx 	69 MPH	= Best Angle of Climb Speed

Vy 	92 MPH	= Best Rate of Climb Speed

Vbest l/d 	85 MPH	= Best Glide (lift/drag), flaps up/down

Vs 	66 MPH	= Stall Speed, normal configuration

Vso 	56 MPH	= Stall Speed, landing configuration

Vfo 	130/105 MPH	= Maximum Flap Extension Speed

Va 	117 MPH	= Maneuvering Speed (at gross weight)

Vno 	155 MPH	= Maximum Structural Cruising Speed

Vne 	185 MPH	= Never Exceed Speed

### 90-100 MPH	= Normal Climb Out

69 MPH	= Short Field T/O, Flaps Flaps 15°

80-90 MPH	= Normal Landing Approach, Flaps Up

70-80 MPH	= Normal Landing Approach, Flaps 40°

70 MPH	= Short Field Approach, Flaps 40°

#### Specifications

2500 lbs	= Maximum Gross Weight

1598 lbs	= Basic Empty Weight

608 lbs	= Payload With Full Fuel

10.0 gph	= Fuel Flow @ 75% Power

50 gal	= Total Fuel Capacity

49 gal	= Total Useable Fuel

100LL	= Fuel Octane Rating (Blue)

8 qts	= Oil Sump Capacity

6 qts	= Minimum Oil Quantity

180 hp	= Lycoming O-360-A1F6

12 V	= Battery